## Slide 1: On Python and Positioning
December 2020
An Introduction to Working with Geospatial Data in Python with GeoPandas

## Slide 2: This Evening’s Quest
Dataset Overview
Python Code Examples
Python Packages
Geospatial Enlightenment!
Sources: - Cover map: Massachusetts. Drawn by S. Lewis. (Boston: Published by Thomas & Andrews. 1812); David Rumsey Historical Map Collection - All clipart, except where noted, is from Clipart-library.com, licensed for personal use
Geospatial Ecosystem & Theory

## Slide 3: Dataset Overview
    Wikipedia’s “Shipwrecks of Massachusetts” page
      https://en.wikipedia.org/wiki/List_of_shipwrecks_of_Massachusetts
      Data format: KML file converted into a shapefile
Shipwrecks of MA
Dive Sites
    DiveSites.com API for sites within 100 nautical miles of Boston, MA
      http://api.divesites.com/docs/
      Data format: JSON
Part of the Massachusetts coastline is known as the “Ocean’s Graveyard”

## Slide 4: The Geospatial Ecosystem: Geographic Information Systems (GIS)
Data Collection
Note: 1. Bolstad, Paul. GIS Fundamentals: a First Text on Geographic Information Systems. 6th ed., XanEdu, 2019.
GIS Software
    Desktop Apps: QGIS, ArcGIS, others
    OSGeo Projects: GDAL/OGR, GEOS
    Python, R packages
A GIS is a computer-based system to aid in the collection, maintenance, storage, analysis, output, and distribution of spatial data and information – this can include hardware, software, data, people, and industry protocols1
Data Storage
Industry Protocols
    Open Geospatial Consortium (OGC)

## Slide 5: Geospatial Data Models
Discrete geometries
Points, lines, polygons, and multipolygons
Shapefile (.shp/.dbf/.shx/.prj)
GeoJSON (.json), KML (.kml)
Geopackage (.gpkg)
Vector
Continuous, “gridded” data
Elevation, satellite images, ground cover
GeoTIFF (.TIF or .TIFF)
Image (.img)
Geopackage (.gpkg)
Raster
Description
File Format Examples
CSV (.csv)
Any attribute tied to a location
Example: Census data by county
Data Attributes

## Slide 6: Coordinate Reference Systems
    Coordinate Reference Systems (CRS) tie 3D coordinates to real world entities
      Based on a Datum (geographic measurements of Earth and assumptions)
    Examples of coordinate reference systems:
      WGS84: US-centric, used for GeoJSON and most web data
      Others: NAD83, ITRF
    Golden rule: know thy data! Know the coordinate system used for your data and convert datasets into the same CRS before combining
      The CRS is like the “unit” of geospatial data
Source: - Longitude and Latitude (left): By Mike1024 - Based on en:File:EarthTangentialPlane.png by en:User:Raffyl99 (public domain), Public Domain, https://commons.wikimedia.org/w/index.php?curid=9510652

## Slide 7: Projections: Translating 3D into 2D
    A projection translates 3D coordinates into a 2D representation
    As one might expect, all projections add an element of distortion
    Different projections preserve/distort different aspects of the geographic features
Source: - Projected map: molumen on the Open Clip Art Library, CC0, via Wikimedia Commons

## Slide 8: Python Geospatial Packages
    General: GeoPandas, pySAL
    Supporting Packages:
      Fiona (vector I/O), Rasterio (raster I/O)
      pyproj (CRS/projection transformations)
      Shapely (implements GEOS geospatial functions)
    Visualizations:
      matplotlib, descartes
      contextily (web tiles)
      folium (leaflet.js), Cartopy
    Geocoding: geoPY

## Slide 9: Code Demo Time!
Web Tiles
Python Magic
Data

## Slide 10: APPENDIX A
Resources

## Slide 11: Resources
    GitHub project repository:
      https://github.com/HKuz/Geospatial_Overview
    Documentation:
      GeoPandas: https://geopandas.org/index.html#
      folium: https://python-visualization.github.io/folium/
    Codes for most commonly used CRSs and projections:
      www.spatialreference.org
    Learn more with the Kaggle Geospatial Analysis course (free):
      https://www.kaggle.com/learn/geospatial-analysis
    Get help via the GIS stack exchange
      https://gis.stackexchange.com/